XSLT 4.0

---
Main Features
- Syntax additions to make code 'terser'
- Enhancements to the type system to allow more expressive constraints, especially for maps and atomic values.
- Type-based pattern matching
- Additional functionality for processing arrays
- Streaming split from the main specification

---
Syntax additions –
increasing XSLT code density
These slide examples will be simple, possibly nonsensical or easier in direct XPath, but illustrative
XSLT 4.0
<xsl:choose>
   <xsl:when test="$n lt $low">
      <xsl:sequence select="../below"/>
   </xsl:when>
   <xsl:when test="$n gt $high">
      <xsl:sequence select="../above"/>
   </xsl:when>
   <xsl:otherwise>
      <xsl:sequence select="../within"/>
   </xsl:otherwise>
</xsl:choose>
XSLT 3.0 code
<xsl:choose>
   <xsl:when test="$n lt $low" select="../below"/>
   <xsl:when test="$n gt $high" select="../above"/>
   <xsl:otherwise select="../within"/>
</xsl:choose>
Terser XSLT 4.0 equivalent

---
XSLT workbench – i
SaxonJS only compiles/runs XSLT 3 and XPath 3.1
Solution:
Convert XSLT 4 to ~equivalent XSLT 3 for a number of new constructs, and run via fn:transform()
Only XSLT syntax is converted
XPath expressions are not converted – XPath 4.0 syntax additions and new/modified functions not supported
Some ~equivalent functions are provided in f: ar: and ma: namespaces
XSLT 3 CODE
XSLT 4.0
XSLT 4 CODE
INPUT
RESULT

---
XSLT workbench – ii
Syntax limitations
map{'a':1,'b':2}
{'a':1,'b':2}
map keyword required in 3, optional in 4
function($x) {$x}
fn($x) {$x}
inline function keyword must be function in 3, can be fn in 4
if(a) then b
else ()
if(a) {b}
if/then/else must be complete in 3,
can use {exp} in 4

---
XSLT workbench – iii
~Equivalent functions
fn:for-each($input as item()*,
        $action as fn(item(), xs:integer) as item()*
) as item()*
<!--QT4FOLib – imported into the XSLT3 stylesheet-->
<xsl:function name="f:for-each" as="item()*">
   <xsl:param name="input" as="item()*"/>
   <xsl:param name="fn" as="function(*)"/>
   <xsl:sequence select="for-each-pair(
     $input,
     1 to count($input),
     $fn)"/>
</xsl:function>
<xsl:sequence select="f:for-each(
  ('a','b','c'),
  function($x,$pos) {$x || $pos}
)"/>
'a1','b2','c3'
Sequence position not supported in XPath 3.1
Hints will be provided when such functions could be helpful; namespace prefixes are already bound in the stylesheet

---
Development/documentation aid
<xsl:stylesheet xmlns:xsl="http://www.w3.org/1999/XSL/Transform"
  main-module="toplevel-uri.xsl" ...>
   <xsl:note role="description">
      <p>This is a note <b>purely</b> for purposes outside XSLT. <br/>
       Think of it as a comment that can contain structured stuff.</p>
   </xsl:note>
   <xsl:function name="t:temp">
      <xsl:note class=”simple”>It can appear anywhere as a child element
        and can have any attributes …
      </xsl:note>
      <xsl:param name="a">
        <xsl:note continuation-of="previous::xsl:note[1]">
        … and is totally ignored by XSLT for any
        syntactic or semantic purposes.</xsl:note>
      </xsl:param>
      …
   </xsl:function>
</xsl:stylesheet>

---
Selection i
@select vs xsl:sequence[@select]
<xsl:choose>
   <xsl:when test="$n lt $low">
      <xsl:sequence select="../below"/>
   </xsl:when>
   <xsl:when test="$n gt $high">
      <xsl:sequence select="../above"/>
   </xsl:when>
   <xsl:otherwise>
      <xsl:sequence select="../within"/>
   </xsl:otherwise>
</xsl:choose>
Similarly for:
xsl:map |
xsl:result-document |
xsl:matching-substring | xsl:non-matching-substring
<xsl:choose>
   <xsl:when test="$n lt $low" select="../below"/>
   <xsl:when test="$n gt $high" select="../above"/>
   <xsl:otherwise select="../within"/>
</xsl:choose>
XSLT 4.0

---
Selection ii
preserving formatted XPath expressions
<xsl:function name="f:book-to-json" as="map(*)">
   <xsl:param name="book" as="element(book)">
   <xsl:sequence select=”
      { ‘title’ : string($book/title),
        ‘author’ : array { $book/author ! string() },
        ‘date’ : let $d := $book/publication return
        if(current-date() lt xs:date($d))
        then $d else ‘Don&apos;t release’
      }”/>
</xsl:function>
<xsl:function name="f:book-to-json" as="map(*)">
   <xsl:param name="book" as="element(book)">
   <xsl:sequence select=”{ ‘title’ : string($book/title),
 ‘author’ : array { $book/author ! string() }, ‘date’ : let
 $d := $book/publication return if(current-date() lt
 xs:date($d)) then $d else ‘Don&apos;t release’}”/>
</xsl:function>
Attribute value normalization

---
Selection iii
preserving formatted XPath expressions
<xsl:function name="f:book-to-json" as="map(*)">
   <xsl:param name="book" as="element(book)">
   <xsl:select>
      { ‘title’ : string($book/title),
        ‘author’ : array { $book/author ! string() },
        ‘date’ : let $d := $book/publication return
        if(current-date() lt xs:date($d))
        then $d else “Don’t release”
      }
   </xsl:select>
</xsl:function>

---
If @then @else
<xsl:choose>
   <xsl:when test="$n ge $low and $n le $high">
      <xsl:apply-templates/>
   </xsl:when>
   <xsl:otherwise>
      <xsl:sequence select="
        error((),'Outside limits')"/>
   </xsl:otherwise>
</xsl:choose>
<xsl:choose>
   <xsl:when test="$n ge 0">
      <xsl:sequence select="1"/>
   </xsl:when>
   <xsl:otherwise>
      <xsl:sequence select="-1"/>
   </xsl:otherwise>
</xsl:choose>
<xsl:if test="$n ge $low and $n le $high"
       else="error((),'Outside limits')">
   <xsl:apply-templates/>
</xsl:if>
<xsl:if test="$n ge 0"
   then="1" else "-1"/>
XSLT 4.0

---
Switch
<xsl:variable name="n" select="a"/>
<xsl:choose>
   <xsl:when test="$n = (1, 2, 3, 4)">
      <xsl:sequence select="../small"/>
   </xsl:when>
   <xsl:when test="$n = (5 to 20)">
      <xsl:sequence select="../medium"/>
   </xsl:when>
   <xsl:otherwise>
      <xsl:sequence select="../large"/>
   </xsl:otherwise>
</xsl:choose>
<xsl:switch select="$n">
   <xsl:when test="1, 2, 3, 4" select="../small"/>
   <xsl:when test="5 to 20" select="../medium"/>
   <xsl:otherwise select="../large"/>
</xsl:switch>

---
Enclosing Mode
<xsl:mode name="M1" on-no-match="shallow-copy"/>
<xsl:template mode="M1" as="element()*" match="p"/>
Lots of other stuff which makes finding all relevant matches difficult
<xsl:template mode="M1" as="element()*" match="/">
  <xsl:apply-templates mode="#current"/>
</xsl:template>
Example
Mode
enclosing modes
<xsl:mode name="M1" as="element()*"
     on-no-match="shallow-copy">
   <xsl:template match="p"/>
 ...
  <xsl:template match="/">
      <xsl:apply-templates/>
   </xsl:template>
</xsl:mode>
XSLT 4.0
mode=M1
for matching
& default mode
for application
<xsl:template match="*" mode="M1"/>
templates in this mode must not appear elsewhere in the package
<xsl:template match="*" mode="#all"/>
only templates inside the mode are applicable – even #all doesn't apply

---
Optional function parameters - i
<xsl:function name="f:inRange">
   <xsl:param name="n"/>
   <xsl:sequence select="f:inRange($n,0)"/>
</xsl:function>
<xsl:function name="f:inRange">
   <xsl:param name="n"/>
   <xsl:param name="low"/>
   <xsl:variable name="high">
      <xsl:call-template name="findNumberLimit"/>
   </xsl:variable>
   <xsl:sequence select="f:inRange($n,$low,$high)"/>
</xsl:function>
<xsl:function name="f:inRange">
   <xsl:param name="n"/>
   <xsl:param name="low"/>
   <xsl:param name="high"/>
   <!-- Stuff -->
</xsl:function>
XSLT 4.0

---
Optional function parameters - ii
<xsl:function name="f:inRange">
   <xsl:param name="n" as="element()"/>
   <xsl:param name="low" required="no" select="0"/>
   <xsl:param name="high" required="no">
      <xsl:call-template name="findNumberLimit"/>
   </xsl:param>
   <!-- Stuff -->
</xsl:function>
XSLT 4.0

---
Named Item Types
<xsl:param name="upscale" as="map(xs:string,function(xs:double) as xs:double)"/>
<xsl:param name="downscale" as="map(xs:string,function(xs:double) as xs:double)"/>
<xsl:variable name="converters" as="map(xs:string,function(xs:double) as xs:double)"
   select="map{
   'double': function ($x) {$x + $x},
   'quadruple': function ($x) {4 * $x}
   }""/>
<xsl:item-type name="f:converters"
as="map(xs:string,function(xs:double) as xs:double)"/>
<xsl:param name="upscale" as="f:converters"/>
<xsl:param name="downscale" as="f:converters"/>
<xsl:variable name="converters" as="f:converters" select="
   map {
   'double': function ($x) {$x + $x},
   'quadruple': function ($x) {4 * $x}
   }"/>

---
Record Types - i
<xsl:record-type name="f:complex" constructor=”true”>
   <xsl:field name="r" as="xs:double"/>
   <xsl:field name="i" as="xs:double" required="no" default="0"/>
</xsl:record-type>
{'r': 0,'i': 1},{'r': 1,'i': 0}
$oneReal,$i
<xsl:variable name="i" as="f:complex" select="f:complex(0, 1)"/>
<xsl:variable name="oneReal" as="f:complex" select="f:complex(1)"/>
Constructor function

---
Record Types - ii
<xsl:record-type name="f:complex" constructor=”true”>
   <xsl:field name="r" as="xs:double"/>
   <xsl:field name="i" as="xs:double" required="no" default="0"/>
</xsl:record-type>
Constructor instruction
<xsl:record r=”$end?x - $start?x” i=”$end?y - $start?y”/>
<xsl:record xsl:as=”f:complex” r=”$end?x - $start?x” i=”$end?y - $start?y”
        xsl:use-when=”$use-records”/>
This is an exception – standard attributes must be in XSLT namespace
{'r': 15, 'i': 12}
Expression evaluated in current context
xs:NCName of key

---
Type-based pattern matching
<xsl:template match="
  .[. instance of array(xs:date)] |
 .[. instance of map(xs:string,*)]”>
<xsl:template match="
 type(array(xs:date)) |
 type(map(xs:string,*))”>
<xsl:template match="
 array(xs:date) |
 map(xs:string,*)”>
record(first, last, *)[?location = 'UK']
matches a map with keys including "first" and "last", and an entry {"location": "UK"}
array(record(first, last, *))[array:size(.) gt 0]
matches a non-empty array where every entry is a map with keys including "first" and "last"
jnode(books, array(record(Author, Title, *)))
matches any JNode of a map entry whose key is "books" and whose content is an array of records, each record having entries keyed "Author" and "Title" (with other entries also allowed)

---
Extension Instructions
to call templates
<xsl:template name="f:report">
   <xsl:param name="code" as="xs:integer" required=”yes”/>
   <xsl:param name="message" as="xs:string?"/>
   <report code="{$code}">{($message,’Emergency’)[1]}</report>
</xsl:template>
<xsl:call-template name="f:report">
   <xsl:with-param name="code" select="123"/>
   <xsl:with-param name="message" select="'All normal'"/>
</xsl:call-template>
… extension-element-prefixes=”f”…
<xsl:template name="f:report"> … </xsl:template/>
<f:report code="123" message="All normal"/>
<f:report code="999"/>
Example
Callable
extension call

---
Fixed namespaces
<xsl:stylesheet
   xmlns:xsl="http://www.w3.org/1999/XSL/Transform"
   xmlns:array="http://www.w3.org/2005/xpath-functions/array"
   xmlns:err="http://www.w3.org/2005/xqt-errors"
   xmlns:fn="http://www.w3.org/2005/xpath-functions"
   xmlns:map="http://www.w3.org/2005/xpath-functions/map"
   xmlns:math="http://www.w3.org/2005/xpath-functions/math"
   xmlns:xs="http://www.w3.org/2001/XMLSchema"
   xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"
   version="3.0">
   <!-- Stuff -->
</xsl:stylesheet>
<xsl:stylesheet
   xmlns:xsl="http://www.w3.org/1999/XSL/Transform"
   fixed-namespaces="#default"
   version="4.0"
   <!-- Stuff -->
</xsl:stylesheet>

---
Separators
<xsl:for-each select="AUTHOR">
   <xsl:sort select="LAST-NAME"/>
   <xsl:sort select="FIRST-NAME"/>
   <xsl:apply-templates select="."/>
   <xsl:if test="position() lt last()">
      <xsl:text>, </xsl:text>
   </xsl:if>
</xsl:for-each>
<xsl:apply-templates select="AUTHOR">
   <xsl:sort select="LAST-NAME"/>
   <xsl:sort select="FIRST-NAME"/>
</xsl:apply-templates>
<xsl:template match="AUTHOR">
   <!-- Stuff -->
   <xsl:if test="position() lt last()">
      <xsl:text>, </xsl:text>
   </xsl:if>
</xsl:for-each>
<xsl:apply-templates select="AUTHOR" separator=", ">
   <xsl:sort select="LAST-NAME"/>
   <xsl:sort select="FIRST-NAME"/>
</xsl:apply-templates>
Similarly for:
xsl:for-each
Michael Kay, John Lumley

---
Grouping – split-when
<xsl:for-each-group select="1 to 4, 5, 7 to 9, 10 to 12, 14, 15, 20 to 22"
      split-when="$next ne ($group[last()] + 1)">
    <a g="{current-group()}"/>
</xsl:for-each-group>
Example
Grouping
split-when: line-wrap
<b g="1 2 3 4 5"/>
<b g="7 8 9 10 11 12"/>
<b g="14 15"/>
<b g="20 21 22"/>
Next item
Group so far

---
xsl:array @for-each
<xsl:variable name="powers" select="
   let $parts := (1 to 4)!
        map{'value':(., . * .,. * . * .)}
  return
    array:for-each(array{$parts},
        function($a){$a?value})"/>
<xsl:variable name="powers" as="array(*)">
   <xsl:array for-each="1 to 4" select="., . * .,. * . * ."/>
</xsl:variable>
<powers>{array:for-each($powers,string-join(?,'-'))}</powers>
Example
Array
array/@for-each
duplicate words
Caution – proposed but not yet fully discussed/agreed
[ (1,1,1),
  (2,4,8),
  (3,9,27),
 (4,16,64) ]
<powers>1-1-1 2-4-8 3-9-27 4-16-64</powers>

---
- xsl:item-type
- For-each and apply-templates separator
- mode/@as
- Extension instructions
- map/@duplicates cf map:build()
- Xsl:for-each-group/@split-when
- Named record types
- Xsl:record
- @select on xsl:map|result-document|when|otherwise|(non-)matching-substring
- Xsl:select
- Self-referential Global variables of function() type
- Parameters passed automatically to apply-imports and next-match
- Optional parameters to xsl:function
- Xsl:switch
- Xsl:note stylesheet/@main-module
- stylesheet/@fixed-namespaces
- Type-based patterns
- Xsl:array
- Enclosing mode
- Shallow-copy-all for map/array trees
- Ordered maps (XPath)

---
Syntax additions
Many of the XSLT syntax additions can be source-converted to XSLT3
A browser-based workbench does this and executes
XSLT 4.0